$m1",0.5",-0.8",-0.4"
$l=0.18"
$j
$d.var pageno,topno,subno,ssno
$d.format page
=$o(,,,-0.5")[]
=$g i4e7"
=$b0.5 $ $ $times14[IMP] $x1"$pageno=pageno+1$v(pageno)$x^(w-1")
=$times14[V3]$ $ $ $b>0
=$c
=$page
$topno=0
$page
$d topic(title)
=$topno=topno+1$subno=0
=$b2,60$x0;$times14[$v(topno).$x;$title]$b^0
$d subtopic(title)
=$subno=subno+1$ssno=0
=$b1,10$x0$h[$v(topno).$v(subno) $u[$title]]$b0
$d subsub='$ssno=ssno+1$b1,10$h[$v(topno).$v(subno).$v(ssno)]'
$d dsubsub='$ssno=ssno+1$b1,10;^ $h[$v(topno).$v(subno).$v(ssno)]'
$d ~='$r8;'
$d ^='$b0$x0$k178$x3;'
$d uu='$list12$u'
$d ll='$list12'
$d ii='$i$list10'
$times12
$t=0.5",1",1.5",2",2.5",3",3.5",4",4.5",5",5.5",6",6.5",7"
$l^0
$times14[IMP Compiler for M68000: Version 3]
$b4 The Compiler translates programs written in the high-level
programming language IMP to M68000 native code.
Compilation is a single pass translation from source to executable code.
$b Reference descriptions of the IMP language are contained in
$h$i[The IMP80 Language] (John Murison, Edinburgh Regional Computing Centre)
and $h$i[The IMP-77 Language]
(Peter S. Robertson, Edinburgh University Computer Science
Department and Lattice Logic Ltd).
The dialect of IMP accepted by the Compiler is closely
similar to IMP-77, and this document provides only an outline
summary of features which are fully covered by
the IMP-77 Report.
A dagger in the margin is used to
flag features which may not be present in IMP-77,
or may be present in different form.
$b In addition to some general-purpose language extensions, a number of extra
features have been included in the present implementation
to extend the capability of the language
for system programming applications.
By their nature these extensions should
be avoided in software which is intended to be portable.
$b2$l>0
Hamish Dewar
CLAN Systems
February 1986
$x*3
$topic'Source program'
$b Source programs are ordinary free format text files. There is no
explicit restriction on line length.
$subtopic'Program order'
$b0.5
The normal ordering in any block
should be declarations, then event trap if any, then instructions.
It is acceptable for $h[static] declarations, such as procedures and
$uu[constant] or $uu[own]
variable declarations, to be interspersed among instructions, but the Compiler
queries any $h[dynamic] variable declarations which appear after
instructions, and hard-faults any which appear in a loop or after a
sequence change.
$b
External specifications (defining imports)
must appear at the outermost textual
level, that is, before the first $uu[begin] or in the main program block.
An external spec may be satisfied by a procedure
occurring later in the same module, that is, it may turn out not to
be an import after all.
This, in a rather unsatisfactory way, allows the same definitions
to be used by importing and exporting modules.
$b
External definitions (defining exports)
must appear in the source file before the main block (if any).
$subtopic'End of file'
$b0.5
A main program file, containing a main block opened with $uu[begin],
may finish with an $uu[end] statement
matching the main block $uu[begin] followed by
end of file. Alternatively it may finish with $uu[end]~$uu[of]~$uu[program].
$b0.3 A program file containing just external procedures but no main
block, or an include file,
is terminated by end of file.
$b0.3
End of file may be either the physical end of the file or the statement
$uu[end]~$uu[of]~$uu[file].
$b0.3
Main program files may also contain external procedures.
$b0.3
If either of the statements $uu[end]~$uu[of]~$uu[program] or
$uu[end]~$uu[of]~$uu[file] is used to terminate a file the Compiler
does not process any subsequent text which there may be in the file.
$subtopic'Line continuation'
$b0.5
As well as the old convention for continuing a statement
onto the following line ($uu[c]), it is permitted to continue a
line by finishing it with a hyphen (minus-sign). The hyphen
must be the very last character on the line.
In addition, a line break is not treated as significant following a
comma or following an equals-sign introducing an array initialisation
sequence.
$subtopic'File inclusion'
$b
Other files may be included in the source by means of the directive:
$b0.3$t4 $uu[include] $ll[".~.~.~.~.~.~.~."]
$b0.5$t2 for example $t4 $uu[include] $ll["GRAPHICS"]
$b
The quoted string specifies the name of the file to be included.
Line numbering in included files operates independently from the main
file, and any Options (see later section) which are specified
within the included file, are localised to this file.
$b
Included files may be nested to a maximum of three.
$subtopic'Conditional compilation'
$b0.5
^ The Compiler implements a conditional compilation mechanism, which
allows parts of the program source to be selected for compilation,
and other parts
ignored, depending on the truth or falsity of controlling
conditions. This simplifies the maintenance of multiple versions
of a program.
$b0.7 A compile-time condition is introduced by the directive
$ll[$$IF] (dollar-sign followed by IF).
It may only appear at a point in the program text
at which a source statement may begin.
The directive is followed
by any valid IMP condition involving only literal expressions.
The effect is that during compilation the condition is evaluated:
if it is true, the following source lines are compiled; if it is
false, they are ignored. The scope of the condition extends
to a matching $ll[$$ELSE] or $ll[$$FINISH] directive.
In the $ll[$$ELSE] case, the following source lines are compiled
if the condition was false, and ignored if it was true.
$b0.7 Compile-time conditions may be nested within one another.
However, it should be noted that excessively elaborate or lengthy
conditional
sections can make the flow of a program for one particular case
difficult to follow. It may be preferable to place long
sections of code which are peculiar to one version in a separate
file, and conditionally include this file.
$b0.7 All conditional-compilation
directives must appear at the start of a source line, apart from
any leading spaces.
Source lines which are not selected for compilation are not
processed in any way. They do not require to be valid IMP.
Consequently quotation and line continuation conventions are not
applied to material which is being skipped.
$b0.7 In Compiler listings, lines which have been skipped are listed
with a minus following the line number as a flag symbol.
$b0.7 Selected material must constitute a number of complete source
statements, but there are no structural restrictions. In particular,
the normal block and statement structure of the language does not
require to be properly nested with respect to the conditional
compilation structure.
$b Simple example:
$b0.5$l0
$ll[
     $uu[constant]~$uu[integer] resident=1, loaded=2   {variant values}
     $uu[constant]~$uu[integer] variant=resident       {that or LOADED}
     .................
     .................
     $$IF variant = loaded                   {is main program}
     $uu[begin]
     $uu[constant]~$uu[integer] max=20000
     $$ELSE                                  {is external}
     $uu[external]~$uu[routine] EDIT($uu[string](255) cliparam)
     $uu[constant]~$uu[integer] max=5000
     $$FINISH]
$topic'Declarations and data types'
$subtopic'Declaration modes'
$b
Data declarations starting with any of the under-noted mode specifications
introduce $h[static] variables. Data declarations without a mode specification
introduce $h[dynamic] variables.
$b0.3
Initialisation values for static variables must be literals.
A static $uu[name] variable may be initialised to $ll[NIL]
by the form $ll['==NIL'],
or to point to an absolute location by the use of an appropriate
store mapping function with literal argument, for
example $ll['$uu[integer]~$uu[name] MODE==INTEGER(126)'].
$subsub $uu[own]
^ $t*1,12[Own variables for which no initial value is specified are $h[not]
initialised to zero. In general, for a normally loaded program, this means
that they are unassigned, although in special cases they may inherit
values from the program environment.]
$subsub $uu[external]
$subsub $uu[constant] or $uu[const]
$b0.3$t*1,12[Constant identifiers of scalar numeric types, but not strings or
structures, may be used in literal expressions.]
$b0 ^ $t*1,12[In a constant declaration declaring multiple
identifiers of ordinal type,
it is permitted to omit the assignment part
(equals-sign
and expression) for any identifier apart from the first. The effect is
that the identifier takes the next value in sequence.]
$dsubsub Explicit address mode
$b0.5
$b0$t*1,12[This low-level mode allows variables to be declared at ($ll[@])
explicitly specified addresses.
The normal alignment requirements which are enforced on automatically
allocated variables are suspended for the first (or sole)
variable declared with this form of mode specification.
It takes either of two forms.
$b0.2$ll[@]~$ii[address-expression]
$b0.2;The $ii[address-expression] is either a literal expression of type
integer or a register-displacement form of assembly-language
effective address.
For example:
$b0$t+ $ll[@126 $uu[byte] MODE]
$b0$t+ $ll[@-32(A5) $uu[integer] ELAPSED]
$b0$t+ $ll[@16_90001 $uu[record](duartf) DUART]
$b0.5
$ll[@~#]~$ii[simple-variable]
$b0.3The effect of this form
is to declare the identifiers in the declaration list
starting at the same address as that of the designated variable.
Successive allocation is at increasing addresses, even if the
designated variable is on stack.]
$b0,40
$subtopic'Declaration attributes'
$b
Attribute keywords appear before the data-type specification
in a declaration. Multiple attribute keywords may appear in any
order.
For example:
$b0.2$ll[
$l0
       $uu[record]~$uu[format] PRINTERF(-
          $uu[byte] MODE,
          $uu[writeonly]~$uu[byte] DATA,
          $uu[volatile]~$uu[half] TIMER,
          $uu[volatile]~$uu[readonly]~$uu[byte] STATUS)]
$b0.5
$dsubsub $uu[readonly]
$b0.3$t*1,12[The $uu[readonly] attribute indicates that a variable
may only be read, not written, by the program. 
It is useful mainly for purposes of documentation, particularly
in application to fields of a record characterising a memory-mapped
device.]
$b0.5
$dsubsub $uu[writeonly]
$b0.3$t*1,12[The $uu[writeonly] attribute indicates that a variable
may only be written to, not read, by the program. 
As well as serving documentation purposes, it indicates that the variable
should not be updated using instructions which imply a read as
well as a write (eg CLR on the M68000).]
$b0.5
$dsubsub $uu[volatile]
$b0.3$t*1,12[For a variable, the $u[volatile] attribute indicates that the
designated location is subject to change independently of the
execution of the program (for example, a timer or device status
register).
For a function, map or predicate, the attribute indicates
that the result is not a pure function of its arguments.
One of the implications is that the Compiler should not
optimise references to such variables and procedures.]
$b0.5
$dsubsub $uu[register] $t5 eg $uu[register]~$uu[integer] $ll[count]
$b0.3$t*1,12[The $uu[register] attribute is valid only for a simple
dynamic variable. It requests that the variable
should be allocated to one of the machine registers available for this
purpose, rather than a storage location, for the sake of efficiency.
At run-time,
the content of the selected register is saved at the point of allocation
and restored on block exit.
$b0 The attribute is ignored if monitoring
diagnostics are in force. Certain restrictions apply to variables
allocated to registers: in particular they may not be used in a
context where the address of the variable is required,
and their values should be regarded as undefined after event trapping
if they have been re-declared in any of the procedures from which
exit has been forced.]
$b0.5
$dsubsub $uu[register]$ll[($ii[register-mnemonic])]
$t6 eg $ $uu[register]$ll[(a2)]~$uu[mite]~$uu[name] $ll[pos]
$b0.3$t*1,12[This is a low-level variant of the preceding attribute in which the
register to be used is specified explicitly. No saving/restoring of
the register content is effected.
$b0 Subsequent to this declaration the register is no longer
treated as eligible for use either as a temporary or user allocatable
register.
This form is valid for parameters to procedures where it indicates
that the parameter
is to be passed, as well as being accessed, in the designated register.
$b0 This is a very low-level feature which should be employed
only where the implications for Compiler register usage have been fully
taken into account.]
$b0,40
$subtopic'Ordinal data types'
$b
$b0$uu[integer]$t4;integer in range -$10[2147483648 (-2$8-[31])] to
$10[2147483647 (2$8-[31]-1)]
$b0$t10;32 bits
$b0$uu[long]~$uu[integer]$t4;accepted as equivalent to $uu[integer]
$b0$t4(with warning message)
$b
$uu[short]$t4;integer in range -32768 to 32767$t10;16 bits
^ $uu[half]$t4;integer in range 0 to 65535$t10;16 bits
^ $uu[mite]$t4;integer in range -128 to 127$t10;8 bits
$b0$uu[byte]$t4;integer in range 0 to 255$t10;8 bits
$b
$uu[integer]$ll[($ii[lo]:$ii[hi])]$t4;integer in range $ii[lo] to $ii[hi]
$t10;8,16,32 bits
$b
^ $uu[char]$t4;character$t10;8 bits
$b0$t*1,12[Traditional IMP does not distinguish characters from integers.
The use of this type permits more appropriate diagnostics,
automatic type transfer,
and better exploitation of over-loading. It also provides compatibility with
Pascal. A value of type $uu[char] may be used wherever a value of type
string is required, by virtue of automatic type conversion from character
to string of length 1. A single character between
string quotes is treated as
of type $uu[char], rather than $uu[string], but like any
other character, subject to automatic type conversion.]
$b
^ $uu[boolean]$t4;boolean (false,true)$t10;8 bits
$b0$t*1,12[The procedure class $uu[predicate] is treated as equivalent
to $uu[boolean]~$uu[function]. An expression of type $uu[boolean] is
a valid form of condition (but conditions are not boolean
expressions). Again this type provides compatibility with Pascal.]
$subtopic'Reals'
$b
$uu[real]$t4;single-precision floating-point$t10;32 bits
$b0$t1;Implementation is by software on M68000
$b
$uu[long]~$uu[real]$t4;treated as $uu[real], apart from type-checking
$subtopic'Strings'
$b
$uu[string]$ll[($ii[maxsize])]$t4;character string $t10;$ii[maxsize]+1 bytes
$b0$t*1,12[For a $uu[name] or $uu[map], $ii[maxsize] may be given as '$ll[*]'
to indicate compatibility
with any string variable, irrespective of its declared maximum size.
This is also permitted in the
case of $uu[string]($ll[*])$uu[array]~$uu[name] parameters to procedures.
$b For a constant string, but not a constant string array,
$ii[maxsize] (and enclosing parentheses) may be omitted,
for example:
$b0$t2 $uu[constant]~$uu[string] $ll[message="TOO MANY NAMES"].]
$b0,40
$subtopic'Records'
$b
$uu[record]~$uu[format] $ii[record-type-ident] (.~.~.~.~.)
$b0.3
$t1;Format declaration introducing a record type
$b
$uu[record]~($ii[record-type-ident])$q
 $ii[record-ident]~,~$ii[record-ident]~,~.~.~.~.
$b0.3
$t1;Record declaration
$b
^ Record construction
$b0.3
A record format identifier may be used as a constructor for the
record type defined by that format, from component values specified in
parentheses
following the format identifier. At present only literal
component values are permitted. This form is particularly useful
for specifying initial values for records, but is not restricted
to that context.
$b0.3 The component values may be
presented either positionally or
using the record component names, preceded by the sub character ($ll[_]),
as keywords.
$b0.3
Example - Format declaration:
$b0.3$t1$ll[$uu[record]~$uu[format] f1($uu[integer] lo,hi, $uu[string](7) code,
$b0$t4 $uu[byte]~$uu[name] where, $uu[short] weight)]
$b
Example - Record declarations with initialisation:
$b0.5$t1$uu[own]~$uu[record]$ll[(f1) r1=0]
$b0.2$t2 meaning: numeric values $ll[=~0], strings $ll[=~"$r4;"],
names $ll[==~NIL]
$b0.7
$b0$t1$ll{$uu[own]~$uu[record](f1) r2=f1(-100,100,"FACTOR",nil,1)
$b0.3$t1$uu[own]~$uu[record](f1) r3=f1(0,,"DUMMY")}
$b0.2$t2 by enumeration, any omitted values unassigned
$b0.7
$b0$t1$ll{$uu[own]~$uu[record](f1) r4=f1(_code="UNDEF",_weight=99)
$b0.3$t1$uu[own]~$uu[record](f1) r5=f1(_hi=99999,_code="MAX")}
$b0.2$t2 by selection using field names, any omitted values unassigned;
$b0.2$t2  field names may appear in any order
$subtopic'Arrays'
$b
Static arrays must have $ii[literal] bounds. Dynamic arrays may have
$ii[literal] or $ii[non-literal] bounds.
Array names may have $ii[literal], $ii[literal unbounded],
$ii[implicit] or $ii[conformant] bounds.
$b0.5
^ The array type information defining the bounds may be placed after the keyword
$uu[array] or after the list of identifiers.
For example:
$b0.2$t1 $uu[integer]~$uu[array]~$ll[(1:5,1:4)] $ll[table]
$t7 or $uu[integer]~$uu[array] $ll[table]~$ll[(1:5,1:4)]
$b0.2$t1 $uu[integer]~$uu[array]~$ll[(0:*)]~$uu[name] $ll[a]
$t7 or $uu[integer]~$uu[array]~$uu[name] $ll[a]~$ll[(0:*)]
$b0.2$t1 $uu[short]~$uu[array]~$ll[(1:$uu[byte] hi)]~$uu[name] c
$t7 or $uu[short]~$uu[array]~$uu[name] c~$ll[(1:$uu[byte] hi)]
$b0.3
The former position
is mandatory for the $ii[implicit] case.
$b0.5
^ As in Pascal, a multi-dimensional array is regarded as
an array of arrays, and
inner slices of it may be used as arrays of lower dimensionality.
For example, if $ll[TABLE] is an array with bounds $ll[(0:3,1:40)],
then $ll[TABLE(0)] is an array with bounds $ll[(1:40)].
$b1,20
$h[Example array declarations]:
$b0.5
Arrays with $ii[literal] bounds:
$b0$t1 $uu[own]~$uu[byte]~$uu[array]~$ll[(1:10)] $ll[power]
$b0$t1 $uu[integer]~$uu[array]~$ll[(1:5,1:4)] $ll[table]
$b1,6
Arrays with $ii[non-literal] bounds:
$b0$t1 $uu[byte]~$uu[array]~$ll[(lo:hi)] $ll[power]
$b0$t1 $uu[integer]~$uu[array]~$ll[(1:max1,1:max2)] $ll[table]
$b1,6
^ Array names with $ii[literal] bounds:
$b0$t1 $uu[integer]~$uu[array]~$ll[(1:1000)]~$uu[name] $ll[a]
$b0$t1 $uu[real]~$uu[array]~$ll[(10:20,~1:30)]~$uu[name] $ll[delta]
$b0.2$t*1,12[In this case, any array assigned to the name must have the
same literal bounds as the name. This is the most efficient form of array name.]
$b1,6
^ Array names with $ii[literal unbounded] bounds:
$b0$t1 $uu[integer]~$uu[array]~$ll[(1:*)]~$uu[name] $ll[a]
$b0$t1 $uu[real]~$uu[array]~$ll[(10:*,]~1:30)~$uu[name] $ll[delta]
$b0.2$t*1,12[In this case all bounds are literal except for
the upper bound of the outermost dimension, specified as '$ll[*]'.
Any array assigned to the name must have the
same literal bounds except for the outermost upper bound, which may
be any value, literal or variable. This form is as efficient as the previous
case, while providing greater flexibility. However, it precludes automatic
bound checking, and a variable declared in this way cannot be onward assigned
to any of the other forms of array name.]
$b1,6
Array names with $ii[implicit] bounds:
$b0$t1 $uu[integer]~$uu[array]$ll[(1)]$uu[name] $ll[a]
$b0$t1 $uu[real]~$uu[array]$ll[(2)]$uu[name] $ll[delta]
$b0.2$t*1,12[Here, no bounds are specified, just the number of
dimensions.
Any array assigned to the name must have the number
of dimensions indicated, with arbitrary bounds.
This allows complete flexibility of bounds,
while preserving the option of automatic bound checking.]
$b1,6
^ Arrays names with $ii[conformant] bounds:
$b0$t1 $uu[integer]~$uu[array]~$ll[(1:$uu[integer] max)]~$uu[name] $ll[a]
$b0$t1 $uu[real]~$uu[array]~$ll[(10:$uu[integer] xdim,~1:$uu[integer] ydim)]$q
~$uu[name] $ll[delta]
$b0$t1 $uu[short]~$uu[array]~$ll[($uu[byte] lo:$uu[byte] hi)]~$uu[name] count
$b0.2$t*1,12[This case, which is similar to the Pascal conformant array concept,
is confined to array names as procedure parameters.  It cannot
be used for array names declared as ordinary variables.
Each bound is either a declared variable or a literal.
Any actual parameter must have the same literal bounds for any bounds
specified as literal. The other bounds cause the declaration of local
variables to which the value of
the corresponding bound of the actual parameter is automatically
assigned at the time of procedure entry.
This case
allows complete flexibility, in a more selective way than the previous case,
and automatically makes available the values of any variable bounds
for use in the procedure.]
$subtopic'Pointer variables'
$b
Pointer variables are declared by including the keyword $uu[name]
after the data-type. For example:
$b0.2$t1 $ll[$uu[byte]~$uu[name] pos
$b0$t1 $uu[own]~$uu[string]~(*)~$uu[name] details
$b0$t1 $uu[record]~(cellinfo)~$uu[name] head,next,last]
$b
The combinations $uu[name]~$uu[array], $uu[array]~$uu[name] and
$uu[name]~$uu[array]~$uu[name] are all permissible but not any
other combinations.
$subsub Untyped pointer variables
$b0.2 Untyped pointer variables are declared by including just the keyword
$uu[name] without a data-type. For example:
$b0.2$t1 $ll[$uu[routine] dump store($uu[name] from, $uu[integer] bytes)]
$b0.2 Pointers of arbitrary type may be name-assigned to such variables.
$b0.5
^ Untyped pointer variables are characterised simply by an address;
they have no type or size information associated with them.
The pre-defined function $ll[SIZEOF] is not applicable to such
variables, nor to variables of type $uu[string]$ll[(*)]$uu[name] or
$uu[record]$ll[(*)]$uu[name].
$subtopic'Labels'
$b
The $uu[label] declaration is optional except for labels which
are forward-referenced in machine-code instructions or ADDR()
expressions.
$subtopic'Dummy identifiers'
$b
^ In an identifier list within a declaration of scalars (not arrays),
it is permitted to use an asterisk ($ll['*']) in place of an
identifier. Storage is allocated in the usual way for the anonymous
variable. The main use of this facility is in record formats
describing memory-mapped devices with non-contiguous fields.
$topic'Procedures'
$subtopic'Procedures as Parameters'
$b Procedures (routine, functions,
and maps) may themselves be passed as parameters
to other procedures. However, it is not permitted by this technique
to circumvent the usual scope rules of block structure. That is, a
procedure A may not be passed as argument to a procedure B unless A
could be called by B directly, with the same effect.
To police this rule, the Compiler requires procedures passed as
parameters to be in scope to the procedures to which they are passed,
not just to be in scope to the point of call.
A procedure $uu[spec] may be used to achieve this in cases where
it would be inconvenient to place the body earlier.
$b0 The application of the rule to external procedures implies
that a procedure passed as a parameter to an external procedure
should itself be external. In this way, the parameter satisfies
the requirement that it could be called directly (through the
external linkage mechanism).
$subtopic'Over-loading'
$b
^ To cover some of the situations in which it is necessary to have
more than one procedure performing essentially the same operation
but on arguments of different types,
it is permitted to declare more than one procedure with the same name.
This may be done provided that each such procedure
can be distinguished from the others
on the basis of the type of its leading (or sole) parameter.
In each case the procedure type must be the same and either the leading
parameters must all be 'value' or they must all be 'name'.
Each procedure apart from the first must include the keyword $uu[alias]
after the procedure type.
For example:
$b0.3$l0
    $ll[$uu[routine] put($uu[string](255) s)]
         :~:~:~:~:~:~:~:
    $uu[end]
$b0.3$l0
    $ll[$uu[routine]~$uu[alias] put($uu[real] x)]
         :~:~:~:~:~:~:~:
    $uu[end]
$b0.3$l0
    $ll[$uu[routine]~$uu[alias] put($uu[integer] i)]
         :~:~:~:~:~:~:~:
    $uu[end]
$b0.3$l0
    $ll[$uu[routine]~$uu[alias] put($uu[char] i)]
         :~:~:~:~:~:~:~:
    $uu[end]
$b0.5 In this case each call on PUT is treated as a call on the
appropriate individual procedure determined by the type of the argument
provided in the call.
The order of matching is on the basis: most recently declared first.
Hence in the examples above, it is relevant that the $uu[integer] case
occurs after the $uu[real] case, since an integer is a valid
argument for a real value parameter, under automatic type conversion.
Similarly, it is relevant that the $uu[char] case follows the
$uu[string] case, since a character is a valid string,
under automatic type conversion.
$b0.5 The procedures do not all require to be in the same block, and
some or all of them may be external. In the case of external procedures,
each case will require to have a unique name for loading
(through external name aliasing).
$topic'Instructions'
$subtopic'Assignment'
$b0.3
^ Entire array assignment is
permitted between two arrays with identical literal
bounds. Array assignment to 0 is permitted for an array of literal bounds.
$subtopic'Routine call'
$b0.3
^ Repeated calls of the same routine may be elided to a single
call, with the successive parameter lists separated by semi-colons.
For example:
$b0.2$t2 $ll[get(i;j;k)]
$b0.2$t2 $ll[put(n;" cases processed in ";t/1000;" seconds";snl)]
$b0.5 This applies only to routines with parameters,
not to other kinds of procedure.
$subtopic'Procedure return'
$b0.3
^ The form $uu[return] $ii[expression] may be used as an alternative
to the $uu[result], or $uu[true]~/~$uu[false],
instruction for specifying the result of a function,
map or predicate.
$subtopic'Jump'
$b0.3
^ The form $uu[goto] is permitted as an alternative to $ll['->'].
$subtopic'Loop control'
$b0.3
^ The instructions $uu[exit] and $uu[continue] may be followed
by a simple decimal constant to identify an outer loop, for example
$uu[exit]~$ll[2] or $uu[continue]~$ll[3].
The default is 1 - the immediately containing loop.
$b0.4
^ The effect of $uu[continue] is to pass control to the head of
the containing loop, where any $uu[while] or $uu[for] control clause is
tested; any $uu[until] clause attached to the $uu[repeat]
at the end of the loop is ignored.
$subtopic'Monitor'
$b0.3
The instruction $uu[monitor] calls the diagnostics package to
monitor the current state of the program. Program execution is resumed
after the call.
$topic'Expressions'
$subtopic'Operators'
$b0.3Infix operators:
$b0$t*1$ll[
$b0$h[+]$t3 addition
$b0$h[-]$t3 subtraction
$b0$h[!]$t3 inclusive-or
$b0$h[!!]$t3 exclusive-or
$b0$h[*]$t3 multiplication
$b0$h[/]$t3 real-division
$b0$h[//]$t3 integer-division
$b0$h[&]$t3 logical-and
$b0$h[$^] or $h[\]$t3 real-exponentiation
$b0$h[$^$^] or $h[\\]$t3 integer-exponentiation
$b0$h[<<]$t3 left-shift
$b0$h[>>]$t3 right-shift]
$b0.5
String infix operator:
$b0$t*1$ll[
$b0$h[.]$t3 concatenation]
$b0.5
Prefix operators:
$b0$t*1$ll[
$b0$h[-]$t3 negation
$b0$h[\] or $h[$~]$t3 logical not]
$b0.5
Relational operators:
$b0$t*1$ll[
$b0$h[=]$t3 equals
$b0$h[#] or $h[<>]$t3 not equals
$b0$h[<]$t3 less than
$b0$h[>]$t3 greater than
$b0$h[<=]$t3 less or equal
$b0$h[>=]$t3 greater or equal
$b0$h[==]$t3 pointer equality
$b0$h[##]$t3 pointer inequality
$b0$h[->]$t3 string resolution]
$subtopic'Literal constants'
$b0.3Decimal and radix-based constants are supported for both integer
and real. Character and string constants are ASCII. EBCDIC constants
are not supported.
$subtopic'Cast'
^ A value of one scalar type may be cast as a value
of another scalar type by using the type identifier of the latter
as a cast constructor. In the case of two ordinal types, the effect is
well-defined provided that the value being cast is within the
ordinal range of the type to which it is being converted.
In other cases, the effect is system dependent.
The form is
$ii[type-identifier]~$ll{[}~$ii[expression]~$ll{]},
for example, $ll{integer["a"]} or $ll{char[nl]} or
$ll{real[16_C8400000]}.
$subtopic'String indexing'
^ Indexing may be applied to a string in the same way as for an array.
The effect of a such a reference, say $ll[S($ii[n])], is to access
the $ii[n]th character of the string. The type of the indexed element
is $uu[char].
$subtopic'Name-relative addressing'
$b0.3
The name-relative addressing facility provides a means of accessing
a sequence of items of the same type in contexts where array
addressing may not be appropriate.
It takes the form of a $uu[name] variable followed by an index value enclosed
in square
brackets. Such an expression denotes a reference to the variable
located that number of elements away from the element identified
by the current assignment to the name variable.
$b
Caution: this is a Low-level facility.
There is no
check on the validity of the references. Use of the facility is, however,
preferable to
the use of store-mapping functions in a similar role, because it preserves
the type identity of the objects denoted.
(The facility is referred to as 'Address modification' in the system
dependent section of the IMP-77 Report).
$b
For example, with the following definitions and assignment:
$b0.5$l0
$ll{
          $uu[record]~$uu[format] PAIR($uu[real] x,y)
          $uu[record](pair)$uu[array] A(1:100)
          $uu[record](pair)$uu[name]  P
          P == A(7)}
$b0.5
the following would hold:
$b0.5$l0
          $ll{P[2]} would denote $ll{A(9)}
          $ll{P[-6]} would denote $ll{A(1)}
          $ll{P == P[1]} would advance $ll{P} to denote $ll{A(8)}
$x*3
$topic'Compilation options'
$b Compiler options are generally established at the outset in the command
used to invoke the Compiler. However, most of them may also be switched on and
off within the program text by means of the $uu[option] directive.
$subtopic'Command parameters'
$b
There is only one obligatory parameter in the command used
to call the Compiler - the first input parameter -
and that is the name of the source program to be compiled.
There is no default file-name extension for the source file-name.
As a matter
of personal preference, programmers may or may not choose to adopt the
extension $ll[.IMP] for IMP programs.
$b
The other, optional, positional parameters are:
$b0.3$l0
$t1;second input $t4$x-4;$ll[-PRE] $t5 pre-definition file to be included before main file
$t1;first output $t4$x-4;$ll[-OFILE] $t5 object code file
$t1;second output $t4$x-4;$ll[-LFILE] $t5 listing file
$subtopic'Option directive'
$b The Option directive provides the means of specifying options within the
source program.
It takes the form of the keyword $uu[option] followed by a quoted string.
For example:
$b0.5$l0
                       $uu[option] $ll["-NOWARN-NOLIST"]
$b
The quoted string consists of a sequence of Option keywords each preceded by
a dash (hyphen).
$b
The effect of most options is localised to the current procedure or block.
That is, at the end of the block, the Options current at the start of the
block are re-instated.
In addition, the use of the $uu[option] directive without a quoted string
causes the state to revert to what it was immediately before the
last $uu[option] directive.
These points do not apply to the global Options
$ll[-EDIT], $ll[-LOG], $ll[-RUN] and $ll[-FORCE].
$b
Caution: indiscriminate variation of checking and diagnostic
options within a program can create confusion for debugging.
$subtopic'Listing control'
$b
By default the Compiler does not produce a listing. If a listing is required,
it is requested either by 
specifying a file-name as the second output parameter
or by including one of the listing option keywords.
Listing to a file, as opposed to listing to the terminal, may be
selected only at the outset, in the command parameters.
$b
The listing file consists
of the text of the source file with added line numbers, and any
fault or warning messages produced during compilation. Line numbering
runs from 1 at the start of the file and 
includes blank lines and
comment lines. Lines in included files are numbered independently,
with an ampersand as an indicator.
$b1,20
Selecting any of the listing options also causes the Compiler to
output $ll[UNUSED] and $ll[UNDERUSED] warnings for identifiers which are
declared but not utilised. These warnings are not produced for certain
classes of identifier, such as $uu[constant] scalars
and $uu[external]
specifications, which are often included as a complete package.
A variable is regarded as underused if (a)
being readable it is never read, or
(b) being writeable it is never written to.
$b
$ll[-LIST] $t3 produce source file listing
$b0.3$t*1,12[The listing name is derived from the
source file-name (without the extension $ll[.IMP] if present).
The extension $ll[.LIS] is applied.]
$b;$ll[-TT] $t3 send listing to terminal
$b
$ll[-MAP] $t3 program map
$b0.3$t*1,12[output information at end of each procedure,
indicating size of code, etc.]
$b1;$ll[-LOG] $t3 print log
$b0.3$t*1,12[print statistics at end of compilation
indicating number of statements,
atoms per statement, identifiers per statement,
time taken, etc.]
$b
 {The remaining listing options may not be available in all releases}
 $b;$ll[-CODE] $t3 code listing
$b0.3$t*1,12[Print hybrid assembly language interpretation
of code generated for each statement.  This is
before address fix-up and branch shortening,
and so does not fully reflect the final code.]
$b;$ll[-DICT] $t3 print dictionary entries for identifiers
$subtopic'Object file control'
$b
By default, the Compiler generates an object file provided that no
errors are detected during compilation.
$b The compiled code is native Motorola 68000 machine-code, ready for
direct execution. The code file starts with a header which identifies
the import and export lists, the code section with main and reset
entry-points, and the diagnostic sections.
$b
If no name is provided explicitly, as the first output parameter,
the name is derived from the
source file-name (without the extension $ll[.IMP] if present).
The extension $ll[.MOB] (for Motorola object) is applied to the object file-name.
$b
The generation of an object file may be suppressed by specifying the
null file-name as the first output parameter.
$b;$ll[-FORCE] $t3 produce object file even if program faulty
$b;$ll[-RUN] $t3 run program after compilation (if supported)
$b0,20
$subtopic'Run-time checks'
$b
Any individual check may be disabled by citing the indicated keyword
preceded by NO, for example $ll[-NOSTRASS] or $ll[-NOCAP].
$b;$ll[-ASS] $t3 include unassigned check on full integers
$b0.5;$ll[-STRASS] $t3 include unassigned check on strings
$b0.5;$ll[-SASS] $t3 include unassigned check on 16-bit values
$b0.5;$ll[-BASS] $t3 include unassigned check on 8-bit values
$b.7
$t*1,12[The unassigned check is implemented by standardising all
newly declared dynamic variables to a fixed pattern which
is an improbable integer value. The check is defaulted off
for variables occupying less than 32 bits
because there is a greater possibility
of the special pattern occurring as a genuine value.
Even so, the probability remains quite low, so that most programs
can benefit for the additional checking implied by specifying
$ll[-SASS] and $ll[-BASS].
$b Defaults for unassigned checks: $ll[-ASS~-STRASS~-NOSASS~-NOBASS]
$b
For the following three cases, violations which involve
only literal operands are detected and rejected at compile-time rather than
run-time.
$b0.7;$ll[-ARR] $t3 include array bound checking
$b0.5;$ll[-OVER] $t3 include overflow check
$b0.5;$ll[-CAP] $t3 include capacity checking on assignment
$b;$ll[-STACK] $t3 include stack over-run check
$b Defaults: $ll[-ARR~-NOOVER~-CAP~-STACK]
$b;$ll[-NOCHECK] $t3 suppress all checks apart from stack over-run
$b;$ll[-NOCHECK-NOSTACK] $t5 suppress all checks
$subtopic'Run-time diagnostic control'
$b;$ll[-DIAG] $t3 generate procedure identification information
$b0.3$t*1,12[This is the basic level of diagnostics, and is implied
by selection of any of the other diagnostic options.
So $ll[-LINE] implies $ll[-DIAG],
as does $ll[-MON], and hence $ll[-NODIAG]
implies both $ll[-NOLINE] and $ll[-NOMON].
In order to disable diagnostics for an individual procedure, $ll[-NODIAG] should be
asserted at the very start of the procedure.
However, if a run-time error does occur in such a procedure when diagnostics
have been selected for other parts of the program, the effect is unpredictable.]
$b0.7;$ll[-LINE] $t3 generate line number identification information
$b0.7;$ll[-MONitor] $t3 generate variable monitoring information
$b0.3$t*1,12[This option requests that tables of identifier information
should be included in the object file to allow the values of variables
to be monitored. It is effective at the point where a variable is declared
and may be freely switched on and off to select some variables and
exclude others.]
$b0.7;$ll[-TRACE] $t3 enable tracing
$b0.3$t*1,12[This causes code to be generated which allows the program to
be executed one line at a time under the control of the Software Front Panel]
$b Default: $ll[-DIAG~-LINE~-MON~-NOTRACE]
$subtopic'Compiler limits'
$b;$ll[-IDents=]$ii[n] $t3 allow for n user idents (default 1200)
$b0.3$t*1,12[The amount of space allowed for storing the text of
identifiers is a function of the number allowed, so that this is
also increased by increasing IDents. The upper limit is about 2500 to
4000 depending on diagnostic options.]
$b0.7;$ll[-KBytes=]$ii[n] $t3 allow for codesize nK (default 64k, max 128k)
$subtopic'Compile-time control'
$b;$ll[-STRICT] $t3 exclude use of non-standard features
$b0.7;$ll[-NONS] $t3 enable warning-free use of non-standard features
$b0.3$t*1,12[Only the first example of the use of any individual
non-standard feature is reported if this option is not enabled
at the point where the feature is first used. This can be used
to provide a degree of selectivity by switching on and off again.]
$b0.7;$ll[-LOW] $t3 enable use of low-level features
$b0.7;$ll[-VOL] $t3 volatile
$b0.3$t*1,12[Causes the Compiler to assume
that functions and predicates are volatile by default]
$b0.7;$ll[-HALF] $t3 restricted multiply/divide
$b0;$ll[-SHORT]
$b0.3$t*1,12[Causes the Compiler to assume
that the arguments for multiply operations and the results of
divide operations are limited to $uu[half] or $uu[short] values
respectively.]
$b0.7;$ll[-WARN] $t3 enable soft warnings
$b0.7;$ll[-EDIT] $t3 enable editing
$b0.3$t*1,12[When selected, the detection of a hard error during
compilation automatically causes control to be transferred to the
editor for possible correction of the error.
Compilation resumes when the edit is closed.]
$b Default: $ll[-NONONS~-NOSTRICT~-NOLOW~-VOL~-NOHALF~-NOSHORT~-WARN~-EDIT]
$x*3,w
$topic'Compiler Error Reports'
$b
Error reports are kept short to economise on screen space.
For reports which relate to a particular component of a statement,
the culprit is identified by a marker at the start of that component.
An asterisk indicates a hard error, a query a soft warning.
$b
$l0
$x0;*$x3;Faulty form$t4;statement part indicated is syntactically faulty
$x0;*$x3;Unknown atom$t4;lexical atom indicated is mis-spelt or unknown
$x0;*$x3;Non-starter$t4;an IMP statement cannot start with the atom indicated
$x0;*$x3;Unknown name$t4;identifier indicated has not been declared
$x0;*?$x3;Duplicate$t4;identifier indicated has already been declared
 $t4; (warning if first declaration is in include file and unused)
$x0;*$x3;Mismatch$t4;parameters in body of procedure do not match spec
$x0;*$x3;Not variable$t4;operand in assignment context is not a variable
$x0;*$x3;Not reference$t4;operand in pointer context is not a reference
$x0;*$x3;Wrong type$t4;expression is of wrong type for context
$x0;*$x3;Wrong class$t4;category of identifier is wrong for context
$x0;*$x3;Not literal$t4;expression in literal context is not literal
$x0;*$x3;No size$t4;inappropriate use of universal, or undefined, type
$x0;*$x3;Inside out$t4;upper bound is less than lower
$x0;*$x3;Endless loop$t4;literal $uu[for] loop cannot terminate
$x0;*?$x3;Out of range$t4;operand value is out of range
$x0;*$x3;Too few args$t4;too few arguments are given for procedure call
$x0;*$x3;Too many args$t4;too many arguments are given for procedure call (or record)
$x0;*$x3;Not in loop$t4;$uu[exit] or $uu[continue] is not within a loop construct
$x0;*$x3;Not in routine$t4;$uu[return] is not within a routine
$x0;*$x3;Not in fn/map$t4;$uu[result] is not within a function or map
$x0;*$x3;Not in pred$t4;$uu[true]~/~$uu[false] is not within a predicate
$x0;*$x3;Not in block$t4;instruction or dynamic declaration at level 0
$x0;*$x3;$ll[%CYCLE] missing$t4;$uu[repeat] encountered with no matching $uu[cycle]
$x0;*$x3;$ll[%REPEAT] missing$t4;$uu[end] reached with unmatched $uu[cycle]
$x0;*$x3;$ll[%START] missing$t4;$uu[finish] or $uu[else] encountered$q
 with no matching $uu[start]
$x0;*$x3;$ll[%FINISH] missing$t4;$uu[end] reached with unmatched $uu[start]
$x0;*$x3;Extra $ll[%ELSE]$t4;$uu[else] encountered matching earlier$q
 unconditional $uu[else]
$x0;*$x3;$ll[%BEGIN] missing$t4;$uu[end] encountered with no matching $uu[begin] or
 $t4; procedure header
$x0;*$x3;$ll[%END] missing$t4;$uu[end]~$uu[of]~$uu[program] or$q
 $uu[end]~$uu[of]~$uu[file] reached with unmatched
 $t4; $uu[begin] or procedure header
$x0;*$x3;Result missing$t4;there is apparently a path to the end of a function,
 $t4; map or predicate which does not specify a result
$x0;?$x3;Not accessible$t4;instruction apparently cannot be executed
$x0;?$x3;$ii[ident] void$t4;identifier appears to be used before a value is$q
 assigned to it
$x0;?$x3;Dubious usage$t4;statement is valid but peculiar (eg$q
 2nd limb
 $t4; of $uu[and] condition is literally false but 1st is not literal
$x0;*?$x3;Out of order$t4;statement appears in incorrect order in block
 $t4; (warning if benign)
$x0;*?$x3;Nonstandard $ii[n]$t4;non-standard language feature$q
 (warning unless $ll[-STRICT])
$x0;?$x3;Low level$t4;low-level language feature
$x0;*?$x3;$ii[ident] missing$t4;forward label or specced identifier$q
 does not appear in block
 $t4; (warning if unused)
$x0;?$x3;$ii[ident]($ii[index]) missing$t4;switch label not accounted for$q
 - taken as at $uu[end]
$x0;*$x3;$ii[n] extra values for $ii[ident]$q
$t4;too many values for $uu[constant] or $uu[own] array
$x0;?$x3;$ii[n] missing values for $ii[ident]$q
 $ too few values for $uu[constant] or $uu[own] array
$x0;*$x3;Faulty operand$t4;incorrect operand type for machine instruction
$x0;*$x3;Wrong size$t4;incorrect operand size for machine instruction
$b1
$subtopic'Complexity errors'
$b0.2
$b0.3
$x0;?$x3;Not supported$t4;facility not implemented (eg $uu[long]~$uu[integer])
$b0.3
$x0;*$x3;Reg not free!$t4;statement cannot be compiled for lack of a register
$b0.3
$x0;*$x3;Out of reach!$t4;operand is outside the range of the machine
$b0$t4; addressing capability
$b0.3
$x0;*$x3;$ii[ident] out of reach!
$t4;call to procedure specified is outside the range
$b0$t4; of the machine addressing capability
$b0.3
$x0;*$x3;Internal error <n>!$t4;consequential error or Compiler fault
$b
The 'out of reach' error reports relate to cases in which an attempt
is made to generate a machine instruction with a displacement which
is outside the range permitted for the instruction addressing mode.
This may occur in the case of assembly language instructions, or
accesses to variables declared with explicit address modes.
It can also occur for automatically generated references.
$b0.5
For example, it can occur as a result of a static ($uu[own]) data storage
requirement in a single module which exceeds
32 kilobytes. It is sometimes possible to overcome this limitation
for a single large array by declaring it
as the final $uu[own], but note that external
specs also require static storage and the space for such a reference
is allocated when and if used, not at the point of declaration.
$b0.5
For references to the code area, including stored constants,
and references to dynamic variables,
the Compiler
uses various techniques to circumvent the $ll[+~-]~32 kilobyte
relative addressing limit of the M68000.
There is a possibility in exceptional cases that these do not succeed, leading
to an 'out-of-reach' report.
If a name is given in the report, it is that of a procedure which is too
distant from one of its calls.
If no name is given, the problem is access to a constant
or variable.
$subtopic'Disastrous errors'
$b
These reports relate to 
internal Compiler storage limits being exceeded. They all
cause compilation to be abandoned.
$b
** Program too big$t5;Total size of the compiled code and constants
$b0$t1 (see Option $ll[-KBytes])$t5;exceeds the maximum allowed for
$b0.3
** Code space exhausted$t5;Size of the code for currently open blocks
$b0$t5;exceeds the maximum allowed for
$b0.3
** Identifiers too big$t5;Total length of all current identifiers exceeds
$b0$t1 (see Option $ll[-IDents])$t5;the maximum allowed for
$b0.3
** Too many identifiers$t5;Number of current identifiers exceeds the
$b0$t1 (see Option $ll[-IDents])$t5;maximum allowed for
$b0.3
** Too many levels$t5;Depth of textual nesting of blocks exceeds
$b0$t5;the maximum permitted (8)
$b0.3
** Too many literals$t5;Internal storage space for literals is exhausted
$b0.3
** Input ended$t5;There is no $uu[endofprogram] or $uu[endoffile]
$b0$t5; statement
$b0.3
** Too many nested includes$t5;There are more than three levels of nesting
$topic'Run-time errors and diagnostics'
$b
Errors detected at run-time are reported through the system's exception
signalling mechanism (also used for IMP 'events').
If an exception is not trapped, the occurrence of the exception is reported
in the form of an error code and text message, and diagnostics are produced.
$b
For most errors, detection at run-time depends on whether particular
checking options were selected at compile-time.
The $h[default] compile-time options include most checks,
but not unassigned checks on variables occupying less than 32 bits nor
overflow checks.
$b0.5
For the fullest level of checking, the options $ll[-SASS~-BASS~-OVER]
should be enabled, over and above the default checks.
$b0.5
If relevant checks are not enabled, an error may manifest itself
in the form of a hardware detected error, such as Bus Error or Illegal
Instruction.
$c
$subtopic'Exception conditions'
$b The detailed distinctions of the sub-classification should not
be taken as definitive. Some cases may be treated as identical by
hardware or software detection mechanisms.
$b$l0
0.$t1 $H[PROGRAM TERMINATION]
$t1 0.0$t2 normal termination ($uu[stop])
$t1 0.1$t2 operator termination
$t1 0.$ii[n]$t2 hardware error (eg address error) $ + $ii[culprit]
$b$l0
1.$t1 $H[OVERFLOW]
$t1 1.1$t2 integer overflow
$t1 1.2$t2 real overflow
$t1 1.3$t2 string overflow (more than 255 characters)
$t1 1.4$t2 division by zero
$b$l0
2.$t1 $H[RESOURCE EXCEEDED]
$t1 2.1$t2 store space exhausted
$t1 2.2$t2 output limit exceeded
$t1 2.3$t2 time limit exceeded
$b$l0
3.$t1 $H[INPUT/OUTPUT ERROR]
$t1 3.1$t2 data transmission error
$t1 3.2$t2 timeout
$t1 3.3$t2 failure to open file
$t1 3.4$t2 failure on other file system operation
$b$l0
4.$t1 $H[INPUT DATA TYPE ERROR]
$t1 4.1$t2 non-numeric char for numeric input $ + $ii[culprit]
$b$l0
5.$t1 $H[INVALID ARGUMENTS]
$t1 5.1$t2 invalid values for $uu[for] loop
$t1 5.3$t2 upper bound less than lower in array declaration
$t1 5.5$t2 illegal exponent for exponentiation $ + $ii[culprit]
$b$l0
6.$t1 $H[RANGE ERROR]
$t1 6.1$t2 value outside range
$t1 6.2$t2 array index out of bounds $ + $ii[culprit]
$t1 6.3$t2 switch index out of bounds $ + $ii[culprit]
$b$l0
7.$t1 $H[STRING RESOLUTION FAILURE]
$b$l0
8.$t1 $H[UNDEFINED VALUE]
$t1 8.1$t2 unassigned variable
$t1 8.2$t2 illegal address
$b$l0
9.$t1 $H[END OF INPUT]
$b$l0
10.$t1 $H[LIBRARY PROCEDURE ERROR]
$b$l0
11-15. $H[GENERAL PURPOSE]
$subtopic'Diagnostics'
$b
Diagnostics are produced following the $h[suspension] of a program
as a result of:
$l0
              the occurrence of a run-time error
              the execution by the program of a $uu[monitor] statement
              a user request for diagnostics
$b0.5
The last case results from the use of the system attention interrupt
(eg $^G or $^T) followed by $ll['.'] (dot) for diagnostics with
termination or $ll['?'] (query) for diagnostics with continuation
$b
The level, and amount, of diagnostic information produced depends on the
diagnostic Options applied to the program at compilation (and to any
modules to which it is linked).
$b
$subsub Procedure trace-back
$b0.5
The basic level of diagnostic information is the procedure trace-back.
This identifies the procedure in which the suspension occurred, then
the procedure from which that was called, and so on up to the level
of program invocation. Each procedure is identified by its name,
and the name of the containing program file.
$b
$subsub Line numbers
$b0.5
If line number diagnostics have been enabled, the line number of
the suspension and each of the calls in the trace-back is also provided.
An ampersand following the line number indicates that the line
belongs to an included file.
$b
$subsub Variable display
$b0.5
If variable monitoring diagnostics have been enabled, the values of
the variables declared at each level of the trace-back are also
displayed.
In the case of a $uu[name] variable, the address of the variable
is displayed as well as the contents. However, $uu[record]~$uu[name]
variables are monitored to one level only.
In the case of an array, the value of the first element only is
displayed.
$b0.5 In all cases, no value is displayed in the case that the variable
appears to be unassigned, just the name of the variable.
$b
$subsub Note
$b0.5
There is always the possibility, when a program goes wrong, that it
will corrupt the
diagnostic information or the program structure on which diagnosis
depends. Similarly, when diagnostics are entered by operator intervention,
it is possible for the program to be suspended in a state
which prevents valid diagnostics from being produced.
The diagnostic interpretation routines attempt to detect abnormalities
of this kind and report on any corruption.
Fortunately, in practice, these are rare occurrences, but the possibility
should be borne in mind.
$b
Another potential source of erroneous diagnostics is when programs
and linked modules have been
compiled with diagnostic options switched off in some parts and on
in others.
In general, diagnostics cannot be guaranteed to succeed if suspension
occurs in a section compiled with diagnostic options disabled.
$topic'Pre-declared procedures'
$b
$l0
$ll[
$uu[integer]~$uu[map]$t4;INTEGER($uu[integer] a)
$uu[real]~$uu[map]$t4;REAL($uu[integer] a)
$uu[string](*)$uu[map]$t4;STRING($uu[integer] a)
$uu[record](*)$uu[map]$t4;RECORD($uu[integer] a)
$uu[byte]~$uu[map]$t4;BYTE or BYTEINTEGER($uu[integer] a)
$uu[short]~$uu[map]$t4;SHORT or SHORTINTEGER($uu[integer] a)
$uu[mite]~$uu[map]$t4;MITE or MITEINTEGER($uu[integer] a)
$uu[half]~$uu[map]$t4;HALF or HALFINTEGER($uu[integer] a)
$uu[byte]~$uu[map]$t4;LENGTH($uu[string](*)$uu[name] s)
$uu[byte]~$uu[map]$t4;CHARNO($uu[string](*)$uu[name] s, $uu[integer] n)
$uu[integer]~$uu[function]$t4;ADDR($uu[name] n)
$uu[string](1)$uu[function]$t4;TOSTRING($uu[integer] k)
$uu[string](255)$uu[function]$t4;SUBSTRING($uu[string](255) s, $uu[integer] from,to)
$uu[integer]~$uu[function]$t4;REM($uu[integer] a,b)
$uu[integer]~$uu[function]$t4;MULDIV($uu[integer] a,b,c)$q
   {A*B//C without overflow}
$uu[integer]~$uu[function]$t4;INTPT($uu[real] x)
$uu[integer]~$uu[function]$t4;INT($uu[real] x)
$uu[real]~$uu[function]$t4;FRACPT($uu[real] x)
$uu[real]~$uu[function]$t4;SQRT($uu[real] x)
$uu[integer]~$uu[function]$t4;CPUTIME                 {in milliseconds}
$uu[name]$t4;NIL
$uu[record]~(*)~$uu[map]$t4;NEW($uu[record]~(*)~$uu[name] n)
$uu[routine]$t4;DISPOSE($uu[record]~(*)~$uu[name] n)
$uu[record]~$uu[format]$t4;EVENTFM($uu[byte] event,sub, $uu[short] line,
$t5;$uu[integer] extra,$uu[string](255) message)
$uu[record](eventfm)$t4;EVENT
$uu[constant]~$uu[integer]$t4;NL
$uu[constant]~$uu[char]$t4;SNL
$uu[integer]~$uu[function]$t4;NEXTSYMBOL
$uu[routine]$t4;READSYMBOL($uu[name] n)
$uu[routine]$t4;PRINTSYMBOL($uu[integer] k)
$uu[routine]$t4;SKIPSYMBOL
$uu[routine]$t4;PRINTSTRING($uu[string](255) s)
$uu[routine]$t4;READ($uu[name] n)
$uu[routine]$t4;WRITE($uu[integer] m, n)
$uu[routine]$t4;PRINT($uu[real] x, $uu[integer] n,m)
$uu[routine]$t4;PRINTFL($uu[real] x, $uu[integer] n)
$uu[routine]$t4;NEWLINE
$uu[routine]$t4;NEWLINES($uu[integer] i)
$uu[routine]$t4;SPACE
$uu[routine]$t4;SPACES($uu[integer] i)
$uu[routine]$t4;SELECT INPUT($uu[integer] n)
$uu[routine]$t4;SELECT OUTPUT($uu[integer] n)
$uu[routine]$t4;CLOSE INPUT
$uu[routine]$t4;CLOSE OUTPUT
$uu[routine]$t4;SET INPUT($uu[integer] pos)
$uu[routine]$t4;SET OUTPUT($uu[integer] pos)
$uu[routine]$t4;RESET INPUT         {equivalent to SET INPUT(0)}
$uu[routine]$t4;RESET OUTPUT        {equivalent to SET OUTPUT(0)}
$uu[integer]~$uu[function]$t4;INSTREAM
$uu[integer]~$uu[function]$t4;OUTSTREAM
$uu[routine]$t4;OPEN INPUT($uu[integer] n, $uu[string](255) S)
$uu[routine]$t4;OPEN OUTPUT($uu[integer] n, $uu[string](255) S)
$uu[string](255)$uu[function]$t4;CLIPARAM
$uu[routine]$t4;PROMPT($uu[string](255) S)
]
$topic'Assembler in IMP'
$b
Sequences of assembly language instructions may be incorporated in an IMP
program at any point. The Option -LOW should be asserted if this facility
is used.
Apart from the usual hazards of machine level programming, there
is the danger of corrupting the environment pre-supposed by the
high-level facilities. For this reason, it is sensible to keep
the use of these instructions to a minimum and to take
particular care in programming these sections.
$subtopic'Syntax'
$b0.5
Assembly language instructions are distinguished from IMP
statements by being prefaced by an asterisk (eg $ll[*MOVE D0,D1]).
They appear within IMP blocks and procedures and are executed
according to the normal flow of control, subject to any
control transfers invoked by the instructions themselves.
IMP conventions for statement termination, labelling and commenting
apply, but otherwise the form of instruction follows closely that
defined under the heading of Assembler Syntax for each individual instruction
in the Motorola M68000 manual.
$b
Machine-level operands are specified using the mnemonics $ll[D0-D7]
and $ll[A0-A7] (or $ll[SP]), and the standard syntax for
effective addressing (<ea>) modes.
Note, however, that any declaration of IMP identifiers which coincide with
the register mnemonics takes precedence.
Immediate, Quick,
and Address register variants of op-codes are selected automatically.
In comparison with full Assembler there are the following omissions:
$t*2[
$b0$x-2[-] most of the Assembler directives are not applicable
$b0$x-2[-] assembly-time expression evaluation is restricted
$b0$x-2[-] size specification in cases where the size is implicit in the op-code
is not in general allowed
$b0$x-2[-] branch size is handled automatically by the Compiler and a size code
is not allowed for branch instructions
$b0$x-2[-] PC-relative modes are not supported explicitly
$b0$x-2[-] the 'current location counter' $ll[*] is not supported
$b0$x-2[-] the special mnemonics USP (User Stack Pointer), SR (Status Register)
and CCR (Condition Code Register) are not supported but the relevant
effects can be achieved by use of the additional op-codes:
$l0
$ll[
            MTCCR <ea>          for      MOVE <ea>,CCR
            MTSR <ea>           for      MOVE <ea>,SR
            MFSR <ea>           for      MOVE SR,<ea>
            MTUSP An            for      MOVE An,USP
            MFUSP An            for      MOVE USP,An
            ATCCR #<data>       for      AND #<data>,CCR
            ATSR #<data>        for      AND #<data>,SR
            ETCCR #<data>       for      EOR #<data>,CCR
            ETSR #<data>        for      EOR #<data>,SR
            OTCCR #<data>       for      OR #<data>,CCR
            OTSR #<data>        for      OR #<data>,SR]
]
$b
The error report 'Faulty operand' indicates use of an invalid
operand for the context, but
the Compiler does not fully check the validity of <ea> modes for the
particular instruction.
$subtopic'Default size-code'
$b0.5
The default 'size' applied is Long (32-bits)
rather than Word (16-bits), which is the manufacturer's default.
The choice is more appropriate for a high-level language in which
the default integer size is 32 bits.
Programmers who regularly use true Assembler
may choose to make a practice of including the size suffix
explicitly for all relevant instructions, to avoid confusion.
$subtopic'Defining temporary registers'
$b0.3
The pseudo-assembler directive $ll[*TEMP] may be used to
define the temporary registers available to the Compiler.
It is followed by a register-list in standard assembler form
(eg $ll[D0-D2/A0-A1]), or 0 to indicate none, or nothing to
indicate the default temporary register set.
$subtopic'IMP identifiers in Assembler'
$b0.5
IMP identifiers may also be used as operands for assembly language
instructions, provided that they are directly addressable (see below).
Record sub-fields and literally selected elements of arrays may also
be accessed provided that the containing structure is directly addressable.
$b
Labels and procedure names may be referenced in the
Branch group of instructions, including $ll[BSR]. The only alternative
form of operand for these instructions is immediate (eg $ll[*BLT #-4]),
the value specified being the machine-level displacement.
Short and long branches are handled automatically (though the
Compiler's CODE listing does not show this).
To access a forward label in an assembly language instruction,
it is neccesary for the label to have been declared by means
of the IMP declaration $uu[label] $ii[label-ident].
$b
$subtopic'Execution environment'
$b The preceding sections have described the forms of assembly language
statements which are syntactically acceptable to the Compiler.
This section provides some information about
the environment of program
execution which is presumed and maintained by the code generated by
the Compiler.
This has a bearing on
the legitimacy and effects of assembly
language statments (and IMP statements involving low-level features).
It should be noted that
this is an area which is subject to change between different versions
and different operating system environments.
$b
The registers defined as available for use as temporaries by the
Compiler (by default D0-D4 and A0-A3),
with the exception of D4,
may be freely used within
assembly sections, but no assumptions can be made about
their contents after execution of most IMP statements.
Other registers may be used only on the basis that their values
are restored before reverting to IMP. In particular this applies
to the stack pointer SP.
In addition, the accessing of local variables may depend on
SP; if SP is changed other than by Compiler-generated code,
the addressing of these variables will be rendered erroneous.
The addressing of global and own variables depends on A4, so that
any modification of this register rules out access to non-local variables.
$subtopic'Directly addressable variables'
$b0.5
The detailed definition of which variables can be directly addressed
(and with what effect) over the whole range of data types
is fairly complex. The following
cases are reasonably straightforward and stable.
Identifiers are directly addressable if they are:
$l0
           declared as own
       or  declared at the outermost level
       or  declared at the current level
       or  declared by means of an explicit address $ll[(@)] declaration
       or  declared as registers
$b0.5
Array identifiers are directly addressable only if they meet the
above requirements $h[and] their bounds are literal $h[and] their size
is 'moderate'.
$b0.5
Variables declared at intermediate levels, and external objects,
should not be
used since an indirection may be involved in accessing them.
In the case of a $uu[name] variable the effective operand is
the pointer value (32-bit address) rather than the referenced
object.